## Slide 1: TELESCOPE CONTROL SYSTEM
K. Nitya -CB.AI.U4AIM24123
B. Pavani Shreeya -CB.AI.U4AIM24106
Ardhra Vinod -CB.AI.U4AIM24105
Hari krishna Iyer -CB.AI.U4AIM24114

## Slide 2
Data Acquisition:
  Imported JPL horizons from Astroquery python package.
  Imported SkyCoord (co-ordinates)from astropy to retrive positions of celestial objects.
DSA Implementation:
  Used arrays to store angles, angular velocities and feedforward terms.
  NumPy arrays is used to handle state space representation, matrix multiplications, simulation data and control input efficiently.

## Slide 3
Linear Quadratic Regulator (LQR) is a feedback control algorithm that utilizes all state variables for optimal control design, where each state variable is multiplied by a gain and summed to generate a single actuation value
LQR ALGORITHM

## Slide 4
ALGORITHM
-> System Dynamics Modeling
    State Space Representation:
A: Defines how state variables change over time.
B: Control input matrix for torque application.
-> Optimal LQR Control
  computes u to minimize:
      Q: State weighting matrix (prioritizes angular precision).
      R: Control effort weighting matrix.
Algebraic Riccati Equation (ARE):
      Solve
P = Solution matrix used to compute optimal control gain

## Slide 5
-> Feedforward Compensation
  Velocity Feedforward: Enhance tracking by compensating for target motion:
​
​
  Integrated into control law:
-> Real-Time Target Tracking Simulation:
  Celestial Position Updates:
  Fetch real-time RA/Dec coordinates of target (e.g., Sirius) using astroquery.
  Time-Delay Simulation:
  Introduce latency with time.sleep() to mimic real-world operation.

## Slide 6
-> Numerical Integration of Dynamics
Runge-Kutta 4th Order (RK4):
    Propagate system states over time:
    Solves nonlinear dynamics with time-varying feedforward terms.
-> Performance Metric
Root Mean Square Error (RMSE):
    Quantify tracking accuracy:

## Slide 7
Tracking Error Over Time:
  The error in theta (blue) and phi (orange) decreases rapidly and stabilizes close to zero.
Telescope Path Over Time:
  The telescope starts from an initial state and gradually corrects its angles toward the target.
Observation: The LQR control effectively stabilizes the telescope and brings it to the desired target with minimal oscillations.

## Slide 8: Thank You